Physical Science

Work   Chapter 4

Work- applying force to make something move

W = F * d            	Work = Force times distance

This link contains more info:    http://www.exploratorium.edu/theworld/energy/joules.html

Machine- a device that helps you do work by changing the size or direction of a force

Power- the amount of work done in a certain period of time

P = W/t           		Power = Work divided by time		P = (F * d) / t

| W = F * d | N = kg * m/s2 |
| --- | --- |
| P = W/t | J = N * m |
| MA = Output/Input | W = J/t |
| Fe * de = Fr * dr | MA= de/dr |
| MA = length/height |  |

# 6 Simple Machines

- Lever, crow bar

- wheel & axle, doorknob

- pulley, flagpole

- inclined plane, wheel chair ramp

- wedge, doorstop

- screw, corkscrew

# Mechanical Advantage

How many times the force applied to a machine is multiplied by the machine

MA = 	Output

Input.

# Levers

# Parts of a

Effort- force you have to apply

Effort Arm- portion of a lever from effort to fulcrum

Effort Distance- Distance from where the effort is applied to the fulcrum

Resistance Arm- portion of a lever from Resistance to fulcrum

Resistance distance - Distance from center of gravity of the resistance to the fulcrum

Resistance- what you want to move

Fulcrum- pivot point (may not always be in the middle)

There are three classes of levers

1st Class Lever

Effort

Resistance

Fulcrum

Example:  Teeter-totter

A 1st Class lever has the Fulcrum in the middle

Advantage: (gain force) High MA	Disadvantage: distance

2nd Class Lever

Effort

Resistance

Fulcrum

Example:  Wheel Barrow

A 2nd Class lever has the Resistance in the middle

Advantage: changes direction of effort	Disadvantage: distance

3rd Class Lever

Effort

Resistance

Fulcrum

Example:  Lower arm

A 3rd Class lever has the Effort in the middle

Advantage: Speed (distance)	Disadvantage: loss of power  (low MA)

Wheel & Axle

Wheel & Axle- wheel that spins with its axle.

MA = de            =   Radius of Wheel

dr                 Radius of Axle

Pulley

Pulley- wheel that is free to spin on its axle.

Fixed – doesn’t move

Moveable – does move

MA = # of ropes holding up the weight

Inclined Plane

Inclined Plane - Flat, sloping surface

MA = length / height